## Slide 1: Efficient implementation of image processing algorithm on ARM v8 processor

## Slide 2: Target Device
Single board computer model - Raspberry Pi 400
SoC specifications-
Broadcom BCM2711 quad-core Cortex-A72
(ARM v8) 64-bit SoC @ 1.8GHz
Memory- 4GB LPDDR4-3200

## Slide 3: SoC Block Diagram

## Slide 4: RGB to Gray conversion
Relatively simple operation
Formula
Gray value = (R *0.2126f + G *0.7152f + B *0.0722f)
R, G, B are Red, Green, and Blue Channel values.

## Slide 5: Performance comparison
Chart: Speedup
| Scalar | SIMD | Scalar(2 Threads) | Scalar(4 Threads) | Scalar(8 Threads) | Scalar(16 Threads) | Scalar(32 Threads)
Series 1 | 1 | 1.218 | 1.9169 | 2.2915 | 2.1074 | 2.1156 | 1.9975
Column1
Column2
Maximum speed up achieved for a scalar implementation with thread level parallelism with 4 threads.

## Slide 6: Implementations
Scalar implementation(Baseline)-
Simple for loop implementation running on a single core.
SIMD Implementation- Taking advantage of data parallel SIMD engine and implement data operations using AArch64 Neon assembly instructions.
OpenMP implementation- Taking advantage of multicore SoC with different no. of threads from 2 to 32.

## Slide 7: Future Exploration
Using different memory map for image file planar or instead of current interleaved.
Combine data and thread level parallelism.
Take cache length and memory hierarchy into account.

## Slide 8: Thank you
Umesh Deshmukh
umeshdeshmukh2024@gmail.com